## Slide 1: Automated Synthesis of Protocols from Flows
Murali Talupur
FormalSim
Sept 30 2015
Joint with: Sandip Ray, John Erickson
Intel

## Slide 2: Skyscrapers and blueprints
Who builds skyscrapers without blueprints?
  Leslie Lamport (REACT 2014) voicing a common frustration among FV practitioners
  We have powerful methods for protocol verification but no models of protocols
So why don’t the architects write executable models given the obvious benefits?
  Lazy and no incentive?

## Slide 3: Informal Specs to Models
Turns out architects do create blueprints but not in the form we expect
  Detailed tables, flow diagrams all glued together with English text instead of executable models
  RTL designers quite happy with it for the last 20+ yrs
With a little bit of massaging it is easy to generate executable models from the design artifacts
  Quick and easy to use
  Fantastic empirical results

## Slide 4: Current Validation Setup
MAS
RTL design
BFM
time
Validation can begin in earnest only when both RTL and BFM are ready
Differing interpretations possible at validation and design ends
Architect
Validator
Designer

## Slide 5: A better way
MAS
RTL design
BFM
HLM
Leverage
HLM
MAS
Clean and
unambiguous
Create executable, high level model which is formally analyzable (HLM)
  Validation can begin early
Leverage this to create validation IP
Designers benefit from having correct, unambiguous reference model
But no viable way to create high level formal models

## Slide 6: Enter Flows
Rich information readily available in design documents
  Tables, state descriptions, Flows
Flows are partial orders on system events
  Such as sending and receiving of messages
  Provide natural descriptions for message passing systems
Succinct and easy to understand
  Even a large protocol has about 40 odd Flows which is orders of magnitude smaller than the protocol itself
Dir
i
ReqS
GntS
Dir
i
ReqE
GntE
ReqShar
ReqExcl
Two Flows from German’s protocol

## Slide 7: Flows with state annotations
Annotate each event with:
  A guard enabling that event
  And updates to states variables
Both are Murphi snippets
Flow language has 3 additional fields:
  What messages to recv
  What messages to send
  Which agent is executing
Dir
i
ReqS
GntS
Guard:
CurrCmd = Empty
Action:
CurrPtr = i
e2
e1
e3
Event e2:
agent: Dir
recv: (ReqS, i)
guard: CurrCmd = Empty
update: CurrPtr := i
send: (GntS, i)
ReqShar Flow

## Slide 8: Flows2HLM
Each event converted to a Murphi rule
  Special functions for sending and receiving messages
  Track flow instantiations and where an agent is in a particular flow instance
  Guards and updates copied into the Murphi rule
Dir
i
ReqS
GntS
Guard:
CurrCmd = Empty
Action:
CurrPtr= i
e2
e1
e3
ruleset i: cbox do
rule “e2”
CurrCmd = Empty & Recv(ReqS, i, tracking_info) & Check_txn_buffer(i)
=>
Begin
CurrPtr := i;
Send(GntS, i, tracking_info);
Update_txn_buffer(i);
End
Corresponding Murphi rule

## Slide 9: Advantages
Book keeping is all free
  Avoids boring code and focuses on aspects most important to architects
    Less chance of making mistakes
Amount of annotation we have to add is tiny compared to the final protocol size
  1:20 ratio typically
Notes: Power of the method comes from two things:
Small amount annotations
Even if annotations become a significant portion of the final Murphi model this still is better than coding directly in Murphi. Just because of the way things are organized, you have to think locally, one flow at a time.

## Slide 10: Advantages
We don’t break the natural organization of a protocol
  Describe what happens within a single logical transaction
  No context switching between Flows
    We just have to describe what an agent does in a given scenario
    In table based and direct coding, we have to consider what an agent can do in different scenarios at once
Intuitive and easy to understand
  Easy to modify and maintain
  We can give enriched flows back to the architect
Flow based modeling allows us to go after large designs and a wide variety of designs

## Slide 11: With Flows based Modeling
MAS
RTL design
BFM
HLM
Leverage
HLM
MAS
Clean and
unambiguous
Getting executable formal models written in Murphi or other high level languages is hard
Our work shows a way around this by working directly with Flows
  Flows are already available in the design documents
  Additional state annotations are easy to supply
Flow
charts
Flows
Low effort!
Automatic!
Flows

## Slide 12: Applications
Several different types of protocols synthesized
  (Server) Cache coherence + Bus Interface Unit protocols
  (Graphics) Cache coherence protocol and a derivative (done by Architect)
  (Server) Link Layer and Bus Lock protocols
  (SoC) Secure Boot Flow
6x faster compared to other modeling efforts
Found several interesting architectural bugs
Provides architects & designers an early indication of protocol complexity

## Slide 13: Related work
Invariants from Flows [FMCAD 2008/09]
  Earlier Flows subsumed by the stronger notion here
Message sequence charts, Live sequence charts
  More emphasis on graphical interface + real time reactive systems
Alur et al [PLDI 2013] using snippets
  Equivalent to tables
Alur et al [CAV 2015] using sample scenarios + FSMs + LTL properties
  Complicated and impractical

## Slide 14: Skyscrapers revisited
RTL :model is similar to skyscraper: scaled down skyscraper
  Writing executable model manually takes a lot of effort
  And the language support is primitive
    Equivalent to building a scaled down skyscraper using wood instead of concrete

## Slide 15: Conclusion
Flows based synthesis shows an easy and effective way to generate models
  Leveraging “blueprints”
Very easy to build your own version of Flows2HLM
  More than >4 versions at Intel
  Couple of months to build a basic version

## Slide 16: The Flows2HLM Method
An effective way of generating executable and formal models
  Leverages information already present in specification documents
  Enables very quick modeling
Early validation becomes possible
Fantastic empirical results

## Slide 17: Skyscrapers revisited
Architects do create blueprints
  Only targeted towards humans, not machines
RTL :model is similar to skyscraper: scaled down skyscraper
  Creating executable model manually takes a lot of effort.
  Plus the language support is primitive.
    Equivalent to building a scaled down skyscraper using wood instead of concrete
Instead we can leverage the rich information already present to generate the model

## Slide 18: Protocol Models from Flows
Once we have Flows generating a model is completely automatic
  We just need a scheduler to fire events in Flows
Advantages:
  Ease: Very easy to use. Almost no entry barrier
  Efficiency: Allows very quick modeling of designs
  Scalability: Can model very large protocols/sets of protocols
  Maintainability: Intuitive to write, understand & maintain
Flow based modeling allows us to go after large designs and a wide variety of designs

## Slide 19: Enter Flows
We can synthesize formal executable models from Flows
Flows are partial orders on system events
  Such as sending and receiving of messages
  Provide natural descriptions for message passing systems
Readily available in design documents
  Architects think in these terms
    Flows in fact can be thought of as specifying the protocol
  Succinct and easy to understand
    Even a large protocol has about 40 odd Flows which is orders of magnitude smaller than the protocol itself
Dir
i
ReqS
GntS
Dir
i
ReqE
GntE
ReqShar
ReqExcl
Two Flows from German’s protocol