## Slide 1: Specification and Scalable Verification of Security Properties in Contemporary SoCs
Pramod Subramanyan
This work was supported in part by CFAR, one of the six SRC STARTnet centers, sponsored by MARCO and DARPA

## Slide 2: Bird’s Eye View of an SoC
On-chip Interconnect
CPU
GPU
Camera
Touch
Flash
DMA
WiFi/3G
SCIP
…
MMU+
DRAM
Microcontroller
Memory
HW accelerators
…
NoC interface
SoC functionality is implemented by a combination of hardware and firmware

## Slide 3: SoC Verification is Challenging
On-chip Interconnect
CPU
GPU
Camera
Touch
Flash
DMA
WiFi/3G
SCIP
…
MMU+
DRAM
FW
Complete verification is not scalable
Separate verification misses bugs!

## Slide 4: Constructing an ILA
; start AES state machine
MOV ACC, #01
MOV DPTR, #0xFF00
MOVX @DPTR, ACC
; poll for completion
wait_finish:
MOV DPTR, #0xFF01
MOVX ACC, @DPTR
CMPI ACC, #00
JNZ wait_finish
IDLE
READ
ENC
WRITE
Instruction-Level Model of µc ISA
Instruction-Level Model of HW accelerators
Instruction-Level Abstraction (ILA) of SoC
Insight: Treat MMIO reads/writes as part of an extended ISA aka ILA

## Slide 5: Synthesizing an ILA
Template abstraction
Synthesis Algorithm
Instruction-Level Abstraction
Simulator
Golden Model
RTL
Model Checker
Refinement Relations
Bugs/counter examples
FW verification
[FMCAD’15]
It’s too hard to manually construct an ILA so synthesize it instead!

## Slide 6: Security Verification is Harder!
SoC
secret
Confidentiality: HW/FW secrets must not leak to untrusted entities
reg
Integrity: Untrusted entities must not influence sensitive registers
Specifying these in LTL is hard!
Not predicates of state, instead these properties refer to information flow!

## Slide 7: Specifying Information Flow Properties
src
dst
HW
model
FW
model
Properties
HW
model
FW
model
aux
state
Original System Model
Augmented System Model
Information flow property specifies that src cannot influence dst
Specified on an augmented ILA
High-level system state such as user/su mode, current thread and VM ids, and son
Convert events such as user/su state-transitions into state variables

## Slide 8: Proving Information Flow Properties
src1
dst1
T
T’
src2
dst2
inp
Can different values at the source result in different values at the destination?
Can we do better with a taint+CEGAR hybrid?
In the security community: static and dynamic taint analysis

## Slide 9: HW/FW Security Concerns are an Important and Exciting Research Area
http://www.wired.com/2015/07/hackers-remotely-kill-jeep-highway/
Come to the poster to talk more!